## Slide 1: Lab 3: DNS Resolver
by Ethan Hurst

## Slide 2: What is a DNS stub resolver?
A DNS stub resolver is a program that converts a domain name like www.example.com into an ip address like 192.0.2.1
  It does this by sending a query to a DNS recursive resolver which does the actual resolving
  Sometimes a domain name will have multiple ip addresses or an alias
www.example.com
DNS stub resolver
DNS recursive resolver
192.0.2.1
Input
Output
Query
Query + resource record(s)
This is all you have to worry about for this lab

## Slide 3: Stuff that you should review
HW 5: Sockets (Especially client.c)
String manipulation
I highly recommend using an IDE with a debugger and/or valgrind! This lab is more difficult than the last one, you’ll probably want to check the contents of your wires with a debugger. I am partial to Clion (it’s free on the lab machines) but Visual Studio works just as well.

## Slide 4: Step 1: Download dnsresolver-handout.tar from Learning Suite
resolver.c
Makefile
resolver-ref
autograde-dnsresolver.py

## Slide 5: Step 2: Analyze the code you’re given
A lot of the functions here are stubs, feel free to use them or delete them, whatever floats your boat
The only function you may not delete is resolve()
Speaking of the main function:

## Slide 6: Step 2: Analyze the code you’re given
A lot of the functions here are stubs, feel free to use them or delete them, whatever floats your boat
The only stub function you should not delete is resolve() because this is called by the main function
Speaking of the main function:
Error checks the command line
Notice the usage

## Slide 7: Step 2: Analyze the code you’re given
A lot of the functions here are stubs, feel free to use them or delete them, whatever floats your boat
The only stub function you should not delete is resolve() because this is called by the main function
Speaking of the main function:
Resolve the domain name (where all of the action takes place)

## Slide 8: Step 2: Analyze the code you’re given
A lot of the functions here are stubs, feel free to use them or delete them, whatever floats your boat
The only stub function you should not delete is resolve() because this is called by the main function
Speaking of the main function:
Iterates through all of the answers and prints them
Answers are in a linked list

## Slide 9: Step 3: Make your query wire
In order to send your query, you have to make a properly formatted byte wire
  A byte wire is just a char[] or char*
00: 27 d6 01 00 00 01 00 00
08: 00 00 00 00 03 77 77 77
10: 07 65 78 61 6d 70 6c 65
18: 03 63 6f 6d 00 00 01 00
20: 01
Byte wire for www.example.com
27 d6
Identification
These 2 bytes are randomly generated
Flags
Each bit represents a flag or code (not important for this lab, can be hardcoded)
01 00
00 01
# Questions
The number of questions in the wire
# Answer Resource Records
The number of answers RR’s in the wire
00 00
# Authority/Additional Resource Records
The number of authority and additional RR’s in the wire (these will always be 0 for this lab)
00 00 00 00
03 77 77 77
07 65 78 61 6d 70 6c 65
03 63 6f 6d 00
Question
The formatted domain name (this is explained in a couple slides)
Use presentation mode if you’re having trouble seeing the colors!
00 01 00
01
Type/Class
Type 1 = IPv4 address, Class 1 = IN, Internet (these can be hardcoded)

## Slide 10: Formatting questions
The question is just a specially formatted string for the domain name
The domain name has to be separated into a series of labels
  Each label is encoded one after the next in the name field
  Before each label, a single byte is used that holds a number indicating the number of characters in the label
  Then, the label's characters are encoded, one per byte
  The end of the name is indicated by a null label, representing the root
03 77 77 77 07 65 78 61 6d 70 6c 65 03 63 6f 6d 00
w w w e x a m p l e c o m
label 1
label 2
label 3
Hint: use strtok()! https://www.geeksforgeeks.org/strtok-strtok_r-functions-c-examples/

## Slide 11: Pro tip: Use a struct to build your wire
Define your own struct that has all of the “header” components of a query (everything before the question)
Fill out all the components of the header and memcpy() it into your wire
  Remember from cs224 that bytes are stored in little endian order, so you have to reverse the order of your bytes in each short
  So instead of header->foo = 0x0001, it should be 0x0100
00
01
AB
CD
87
65
struct dns_query_header *header
header->foo =
header->baz =
header->bar =
= 0x0100
= 0xCDAB
= 0x6587
00
01
AB
CD
87
65
(unsigned char*)header

## Slide 12: Test what you have!
Make sure to use to show if you are making your query correctly
Use the command to test your resolver
Your output should looks something like this (the first 2 bytes will be different):

## Slide 13: Step 4: Send your query
listen
This is where your code from HW 5 will come in handy!
The address (host and port) of the server should come from the main function
Your stub resolver should set up a client connection to the recursive resolver
  If your query was formatted correctly, you should have a response in your read buffer
Client
TCP Server
socket
read
write
read
write
Connection
request
read
close
close
EOF
accept
connect
socket
bind
getaddrinfo
getaddrinfo
UDP Server
Use presentation mode!
getaddrinfo
socket
bind
read
write
In homework 5, you converted a UDP server into a TCP server. You also modified a client to read from a file and write to a file.
In the lab, you’ll use UDP as your connection protocol. I recommend downloading the HW 5 handout again and using the unmodified client.
Don’t worry about the server side of the connection.
sendto
recvfrom

## Slide 14: Test what you have!
Again, use to display the response from the server
Use the command to test your resolver
It should look something like this:

## Slide 15: Step 5: Make a single answer
Making the complete answer list will most likely be the toughest part of the lab for you
Let’s begin by analyzing the response from the server
00: 27 D6 81 80 00 01 00 01
08: 00 00 00 00 03 77 77 77
10: 07 65 78 61 6D 70 6C 65
18: 03 63 6F 6D 00 00 01 00
20: 01 C0 0C 00 01 00 01 00
28: 00 05 CA 00 04 5D B8 D8
30: 22
27 D6 81 80 00 01
00 00 00 00 03 77 77 77
07 65 78 61 6D 70 6C 65
03 63 6F 6D 00 00 01 00
01
C0 0C
00 01
Use presentation mode if you’re having trouble seeing the colors!
Query
This should be the same as the query you sent from part 3
NOTICE
The # of answer resource records is now 1
Name
The name that this record belongs to, encoded using compression encoding (more on this in step 7)
00 01
Type/Class
Type 1 = IPv4 address, Class 1 = IN, Internet
00 01
00
00 05 CA
TTL (Time To Live)
Indicates how long this record should stay in the resolver’s cache (you resolver doesn’t have a cache, so don’t worry about this)
00 04
Data Length
The length of the data in this record
Data
Byte (NOT ASCII) encoding of the IPv4 address (can vary in length)
5D B8 D8
22

## Slide 16: Step 5: Make a single answer
Instead of trying to do everything at once, let’s take some baby steps
Make a new answer struct with the data from the first resource record
  As long as the number of RR’s is >0, you can assume that the first resource record will always immediately follow the query
  If there are no RR'
Set the next pointer of your answer to NULL and return this to the main
Type to run the auto-grader, your final output should look like this:

## Slide 17: Step 6: Make an answer list
Let’s take a look at another response, this time for byu.edu
00: 45 FF 81 80 00 01 00 04 08: 00 00 00 00 03 62 79 75 10: 03 65 64 75 00 00 01 00 18: 01 C0 0C 00 01 00 01 00 20: 00 19 96 00 04 80 BB 10 28: 62 C0 0C 00 01 00 01 00 30: 00 19 96 00 04 80 BB 10 38: 64 C0 0C 00 01 00 01 00 40: 00 19 96 00 04 80 BB 10 48: 63 C0 0C 00 01 00 01 00 50: 00 19 96 00 04 80 BB 10 58: 65
Notice how there are 4 answer resource records

## Slide 18: Step 6: Make an answer list
This time a single answer won’t suffice, so you have to make a linked list of answers
You’ll need to keep track of: the head of your answer list, the current answer you’re on, and the index of start of the current resource record
00: 45 FF 81 80 00 01 00 04 08: 00 00 00 00 03 62 79 75 10: 03 65 64 75 00 00 01 00 18: 01 C0 0C 00 01 00 01 00 20: 00 19 96 00 04 80 BB 10 28: 62 C0 0C 00 01 00 01 00 30: 00 19 96 00 04 80 BB 10 38: 64 C0 0C 00 01 00 01 00 40: 00 19 96 00 04 80 BB 10 48: 63 C0 0C 00 01 00 01 00 50: 00 19 96 00 04 80 BB 10 58: 65
Index = 19
Use presentation mode!
Name
Type
Class
TTL
Length
Data
NULL
00 01
00 01
00 00 19 96
00 04
80 BB 10 62
struct dns_rr *
Value
Next
NULL
NULL
Head
Value
Next
NULL
NULL
Start by allocating space for the head of your linked list. Set the current pointer to the head of the list.
Current
00: 45 FF 81 80 00 01 00 04 08: 00 00 00 00 03 62 79 75 10: 03 65 64 75 00 00 01 00 18: 01 C0 0C 00 01 00 01 00 20: 00 19 96 00 04 80 BB 10 28: 62 C0 0C 00 01 00 01 00 30: 00 19 96 00 04 80 BB 10 38: 64 C0 0C 00 01 00 01 00 40: 00 19 96 00 04 80 BB 10 48: 63 C0 0C 00 01 00 01 00 50: 00 19 96 00 04 80 BB 10 58: 65
Set the index to the first byte of the first resource record. This is the size of your query.
Parse the resource record into a dns_rr struct. Don’t worry about parsing the name of the record! You’ll do this in the next step.
Convert the data into an ASCII string. (sprintf() is helpful here) Set the current answer’s value to this string.
Value
Next
128.187.16.98
NULL
Allocate space for the next answer. Set the current’s next value to the allocated pointer, and then set the current to the next answer.
Value
Next
128.187.16.98
<pointer>
Move the index to the first byte of the next record. You’ll have to take the length of the data into account when adding to your index. (The index is represented here in hexadecimal, NOT decimal)
Index = 19 + strlen(name) /*Assume this is 2 for now*/ + sizeof(type) + … + sizeof(length) + length = 29
00: 45 FF 81 80 00 01 00 04 08: 00 00 00 00 03 62 79 75 10: 03 65 64 75 00 00 01 00 18: 01 C0 0C 00 01 00 01 00 20: 00 19 96 00 04 80 BB 10 28: 62 C0 0C 00 01 00 01 00 30: 00 19 96 00 04 80 BB 10 38: 64 C0 0C 00 01 00 01 00 40: 00 19 96 00 04 80 BB 10 48: 63 C0 0C 00 01 00 01 00 50: 00 19 96 00 04 80 BB 10 58: 65
Index = 29
Name
Type
Class
TTL
Length
Data
NULL
00 01
00 01
00 00 19 96
00 04
80 BB 10 64
struct dns_rr *
Value
Next
128.187.16.100
NULL
Repeat the previous steps until the last record.
Value
Next
128.187.16.100
<pointer>
Value
Next
NULL
NULL
Current
Index = 39
00: 45 FF 81 80 00 01 00 04 08: 00 00 00 00 03 62 79 75 10: 03 65 64 75 00 00 01 00 18: 01 C0 0C 00 01 00 01 00 20: 00 19 96 00 04 80 BB 10 28: 62 C0 0C 00 01 00 01 00 30: 00 19 96 00 04 80 BB 10 38: 64 C0 0C 00 01 00 01 00 40: 00 19 96 00 04 80 BB 10 48: 63 C0 0C 00 01 00 01 00 50: 00 19 96 00 04 80 BB 10 58: 65
Name
Type
Class
TTL
Length
Data
NULL
00 01
00 01
00 00 19 96
00 04
80 BB 10 63
struct dns_rr *
Value
Next
128.187.16.99
NULL
Value
Next
NULL
NULL
Value
Next
128.187.16.99
<pointer>
Current
Index = 49
00: 45 FF 81 80 00 01 00 04 08: 00 00 00 00 03 62 79 75 10: 03 65 64 75 00 00 01 00 18: 01 C0 0C 00 01 00 01 00 20: 00 19 96 00 04 80 BB 10 28: 62 C0 0C 00 01 00 01 00 30: 00 19 96 00 04 80 BB 10 38: 64 C0 0C 00 01 00 01 00 40: 00 19 96 00 04 80 BB 10 48: 63 C0 0C 00 01 00 01 00 50: 00 19 96 00 04 80 BB 10 58: 65
Name
Type
Class
TTL
Length
Data
NULL
00 01
00 01
00 00 19 96
00 04
80 BB 10 65
struct dns_rr *
Value
Next
128.187.16.101
NULL
Since this is the last record, you don’t need to allocate space for another answer. The last thing to do is return the head of the list.

## Slide 19: Test what you have!
Use the command
make test

## Slide 20: Step 7: Handle CNAME records
CNAME records have type 5 instead of type 1
Here is a response from the domain www.byu.edu that contains a CNAME record
Notice how the record names change after the CNAME record, they now refer to the alias from the first record
00: B8 CF 81 80 00 01 00 05 08: 00 00 00 00 03 77 77 77 10: 03 62 79 75 03 65 64 75 18: 00 00 01 00 01 C0 0C 00 20: 05 00 01 00 00 16 96 00 28: 09 06 6D 67 2D 77 65 62 30: C0 10 C0 29 00 01 00 01 38: 00 00 16 96 00 04 80 BB 40: 10 65 C0 29 00 01 00 01 48: 00 00 16 96 00 04 80 BB 50: 10 63 C0 29 00 01 00 01 58: 00 00 16 96 00 04 80 BB 60: 10 62 C0 29 00 01 00 01 68: 00 00 16 96 00 04 80 BB 70: 10 64
The first record has type 5 instead of type 1, this means the data is an alias for the query name (question)
All resource records use compression encoding, about time we learned what this is

## Slide 21: Decoding record names
Record names are usually encoded using compressions encoding
Instead of a DNS name encoded as a combination of labels and label-lengths, a two-byte subfield is used to represent a pointer to another location in the message where the name can be found
  The first two bits of this subfield are set to one (the value “11” in binary)
  The remaining 14 bits contain an offset that species where in the message the name can be found
    The first byte of the message (the first byte of the ID field) counts as 0
A regular (non-pointer) label has to be less than 64 bytes, otherwise it would trigger compression encoding
1100 0000 0000 1100
c0
0c
Offset
03 77 77 77 07 65 78 61 6d 70 6c 65 03 63 6f 6d 00
w w w e x a m p l e c o m

## Slide 22: Decoding record names
Name = mg-web.byu.edu.
Name = mg-web.byu.edu
Name = mg-web.byu.ed
Name = mg-web.byu.e
Name = mg-web.byu.
Name = mg-web.by
Name = mg-web.b
Name = mg-web.
Name = mg-we
Name = mg-w
Name = mg-
Name = mg
Name = m
Let’s focus on decoding one of the record names from www.byu.edu
00: B8 CF 81 80 00 01 00 05 08: 00 00 00 00 03 77 77 77 10: 03 62 79 75 03 65 64 75 18: 00 00 01 00 01 C0 0C 00 20: 05 00 01 00 00 16 96 00 28: 09 06 6D 67 2D 77 65 62 30: C0 10 C0 29 00 01 00 01 38: 00 00 16 96 00 04 80 BB 40: 10 65 C0 29 00 01 00 01 48: 00 00 16 96 00 04 80 BB 50: 10 63 C0 29 00 01 00 01 58: 00 00 16 96 00 04 80 BB 60: 10 62 C0 29 00 01 00 01 68: 00 00 16 96 00 04 80 BB 70: 10 64
C0
29
32
33
06
6D
67
2D
77
65
62
29
2A
2B
2C
2D
2E
2F
C0
10
30
31
03
62
79
75
10
11
12
13
03
65
64
75
14
15
16
17
00
18
Name =
Start at the first byte of your record name. For each label: on the first byte, if the first two bits are 11, then the next 14 bits are a pointer to the next label.
You’ll want to use bit masking/shifting to check the first two bits and isolate the pointer.
00: B8 CF 81 80 00 01 00 05 08: 00 00 00 00 03 77 77 77 10: 03 62 79 75 03 65 64 75 18: 00 00 01 00 01 C0 0C 00 20: 05 00 01 00 00 16 96 00 28: 09 06 6D 67 2D 77 65 62 30: C0 10 C0 29 00 01 00 01 38: 00 00 16 96 00 04 80 BB 40: 10 65 C0 29 00 01 00 01 48: 00 00 16 96 00 04 80 BB 50: 10 63 C0 29 00 01 00 01 58: 00 00 16 96 00 04 80 BB 60: 10 62 C0 29 00 01 00 01 68: 00 00 16 96 00 04 80 BB 70: 10 64
00: B8 CF 81 80 00 01 00 05 08: 00 00 00 00 03 77 77 77 10: 03 62 79 75 03 65 64 75 18: 00 00 01 00 01 C0 0C 00 20: 05 00 01 00 00 16 96 00 28: 09 06 6D 67 2D 77 65 62 30: C0 10 C0 29 00 01 00 01 38: 00 00 16 96 00 04 80 BB 40: 10 65 C0 29 00 01 00 01 48: 00 00 16 96 00 04 80 BB 50: 10 63 C0 29 00 01 00 01 58: 00 00 16 96 00 04 80 BB 60: 10 62 C0 29 00 01 00 01 68: 00 00 16 96 00 04 80 BB 70: 10 64
The first 2 bits of this label are 00, so this is just a normal label of length 6. Copy the following 6 bytes into your string and add a period at the end.
00: B8 CF 81 80 00 01 00 05 08: 00 00 00 00 03 77 77 77 10: 03 62 79 75 03 65 64 75 18: 00 00 01 00 01 C0 0C 00 20: 05 00 01 00 00 16 96 00 28: 09 06 6D 67 2D 77 65 62 30: C0 10 C0 29 00 01 00 01 38: 00 00 16 96 00 04 80 BB 40: 10 65 C0 29 00 01 00 01 48: 00 00 16 96 00 04 80 BB 50: 10 63 C0 29 00 01 00 01 58: 00 00 16 96 00 04 80 BB 60: 10 62 C0 29 00 01 00 01 68: 00 00 16 96 00 04 80 BB 70: 10 64
On the next label, the first 2 bits are 11, so this label is a pointer.
00: B8 CF 81 80 00 01 00 05 08: 00 00 00 00 03 77 77 77 10: 03 62 79 75 03 65 64 75 18: 00 00 01 00 01 C0 0C 00 20: 05 00 01 00 00 16 96 00 28: 09 06 6D 67 2D 77 65 62 30: C0 10 C0 29 00 01 00 01 38: 00 00 16 96 00 04 80 BB 40: 10 65 C0 29 00 01 00 01 48: 00 00 16 96 00 04 80 BB 50: 10 63 C0 29 00 01 00 01 58: 00 00 16 96 00 04 80 BB 60: 10 62 C0 29 00 01 00 01 68: 00 00 16 96 00 04 80 BB 70: 10 64
This is a normal label, so we add 3 bytes to our string.
00: B8 CF 81 80 00 01 00 05 08: 00 00 00 00 03 77 77 77 10: 03 62 79 75 03 65 64 75 18: 00 00 01 00 01 C0 0C 00 20: 05 00 01 00 00 16 96 00 28: 09 06 6D 67 2D 77 65 62 30: C0 10 C0 29 00 01 00 01 38: 00 00 16 96 00 04 80 BB 40: 10 65 C0 29 00 01 00 01 48: 00 00 16 96 00 04 80 BB 50: 10 63 C0 29 00 01 00 01 58: 00 00 16 96 00 04 80 BB 60: 10 62 C0 29 00 01 00 01 68: 00 00 16 96 00 04 80 BB 70: 10 64
00: B8 CF 81 80 00 01 00 05 08: 00 00 00 00 03 77 77 77 10: 03 62 79 75 03 65 64 75 18: 00 00 01 00 01 C0 0C 00 20: 05 00 01 00 00 16 96 00 28: 09 06 6D 67 2D 77 65 62 30: C0 10 C0 29 00 01 00 01 38: 00 00 16 96 00 04 80 BB 40: 10 65 C0 29 00 01 00 01 48: 00 00 16 96 00 04 80 BB 50: 10 63 C0 29 00 01 00 01 58: 00 00 16 96 00 04 80 BB 60: 10 62 C0 29 00 01 00 01 68: 00 00 16 96 00 04 80 BB 70: 10 64
When you reach the 0 label, delete the last period from your string. Return the completed string.

## Slide 23: Step 7: Handle CNAME records
Index = 62
Index = 32
Index = 1D
Value
Next
NULL
NULL
Now you have to modify your code from step 6 to handle CNAME records
You’ll need to keep track of more variable: qname
00: B8 CF 81 80 00 01 00 05 08: 00 00 00 00 03 77 77 77 10: 03 62 79 75 03 65 64 75 18: 00 00 01 00 01 C0 0C 00 20: 05 00 01 00 00 16 96 00 28: 09 06 6D 67 2D 77 65 62 30: C0 10 C0 29 00 01 00 01 38: 00 00 16 96 00 04 80 BB 40: 10 65 C0 29 00 01 00 01 48: 00 00 16 96 00 04 80 BB 50: 10 63 C0 29 00 01 00 01 58: 00 00 16 96 00 04 80 BB 60: 10 62 C0 29 00 01 00 01 68: 00 00 16 96 00 04 80 BB 70: 10 64
00: B8 CF 81 80 00 01 00 05 08: 00 00 00 00 03 77 77 77 10: 03 62 79 75 03 65 64 75 18: 00 00 01 00 01 C0 0C 00 20: 05 00 01 00 00 16 96 00 28: 09 06 6D 67 2D 77 65 62 30: C0 10 C0 29 00 01 00 01 38: 00 00 16 96 00 04 80 BB 40: 10 65 C0 29 00 01 00 01 48: 00 00 16 96 00 04 80 BB 50: 10 63 C0 29 00 01 00 01 58: 00 00 16 96 00 04 80 BB 60: 10 62 C0 29 00 01 00 01 68: 00 00 16 96 00 04 80 BB 70: 10 64
Name
Type
Class
TTL
Length
Data
www.byu.edu
00 05
00 01
00 00 16 96
00 09
mg-web.byu.edu
struct dns_rr *
qname = www.byu.edu
Index =
Head
Current
Value
Next
mg-web.byu.edu
NULL
Value
Next
NULL
NULL
Value
Next
128.187.16.99
<pointer>
Value
Next
128.187.16.98
<pointer>
Value
Next
128.187.16.100
NULL
To start, qname should be the same as the query.
Name
Type
Class
TTL
Length
Data
www.byu.edu
00 05
00 01
00 00 16 96
00 09
mg-web.byu.edu
This record has type 5 instead of type 1, which means that the data isn’t an IP address, but rather a CNAME (alias).
Name
Type
Class
TTL
Length
Data
www.byu.edu
00 05
00 01
00 00 16 96
00 09
mg-web.byu.edu
You can use the same function you used to decode the name for the data, the rule of compression encoding are the same.
Set the current’s value to the data and change qname to the new alias.
qname = mg-web.byu.edu
Value
Next
mg-web.byu.edu
<pointer>
00: B8 CF 81 80 00 01 00 05 08: 00 00 00 00 03 77 77 77 10: 03 62 79 75 03 65 64 75 18: 00 00 01 00 01 C0 0C 00 20: 05 00 01 00 00 16 96 00 28: 09 06 6D 67 2D 77 65 62 30: C0 10 C0 29 00 01 00 01 38: 00 00 16 96 00 04 80 BB 40: 10 65 C0 29 00 01 00 01 48: 00 00 16 96 00 04 80 BB 50: 10 63 C0 29 00 01 00 01 58: 00 00 16 96 00 04 80 BB 60: 10 62 C0 29 00 01 00 01 68: 00 00 16 96 00 04 80 BB 70: 10 64
Name
Type
Class
TTL
Length
Data
mg-web.byu.edu
00 01
00 01
00 00 16 96
00 04
128.187.16.101
struct dns_rr *
Notice how the qname and record name are the same
If the record name is ever different from qname, return NULL instead of the head of your answer list.
Name
Type
Class
TTL
Length
Data
mg-web.byu.edu
00 01
00 01
00 00 16 96
00 04
128.187.16.101
Value
Next
128.187.16.101
NULL
Otherwise, handle type 1’s the same way you did in step 6.
Value
Next
128.187.16.101
<pointer>
00: B8 CF 81 80 00 01 00 05 08: 00 00 00 00 03 77 77 77 10: 03 62 79 75 03 65 64 75 18: 00 00 01 00 01 C0 0C 00 20: 05 00 01 00 00 16 96 00 28: 09 06 6D 67 2D 77 65 62 30: C0 10 C0 29 00 01 00 01 38: 00 00 16 96 00 04 80 BB 40: 10 65 C0 29 00 01 00 01 48: 00 00 16 96 00 04 80 BB 50: 10 63 C0 29 00 01 00 01 58: 00 00 16 96 00 04 80 BB 60: 10 62 C0 29 00 01 00 01 68: 00 00 16 96 00 04 80 BB 70: 10 64

## Slide 24: Test what you have!
You should now be able pass most, if not all the tests